## Slide 1
Utah Division of Water Rights
June 21, 2004
What You Need to Know
Willa Knight—April 2018
Making Applications

## Slide 2: Application Agenda
Discuss water right policy by area;
Readiness for filing a complete application;
Introduce the Public Land Survey system;
Discuss duty, diversion, and other use calculations, and;
Make an application map.
Questions
Notes: Perhaps talk about which applications result in a start card. Also talk about surface wells and when a water right must be associated with a well.

## Slide 3: Policy By Area
Water Right

## Slide 4: Helpful Database Tools
“Policies by Water Right Area” is located on the bottom right of the Division’s home page.
This will provide a basic overview for each water right area, including information that may be helpful for an applicant to review before filing an application.
www.waterrights.utah.gov

## Slide 5
Surface and Ground Water :
…Valley locations are open for ground-water applications, which are limited to the domestic use of one family, the irrigation of .25 acre, and 10 livestock.
Notes: Use internet (backup slide)

## Slide 6
Filing Applications
The Details of

## Slide 7: Elements Common to all Applications
The applicant’s name, address and ownership interest;
Source of water;
  Specific spring, stream, or underground well
Flow (cfs), or volume (acre-feet) of water to be diverted;
Point of diversion (POD);
  Where the water will be diverted from the natural source
Beneficial use of the water;

## Slide 8
Place of use (POU);
  Location where the beneficial use will occur
Application map, to identify specific parcels on which the beneficial use will occur;
Signatures of all applicants/owners or legal agents;
Filing fee.

## Slide 9: What You Need to Know
Basis of the water right
  New water right
  Existing water right
  Contract
  Shares in a company
Points of diversion
Places of use
Uses of the water
Notes: Do a sample walk through of applications to tie this idea to Clark’s ppt.
“You want to file a change application. Great. What existing water right will you use? Where will you divert? Where will you use the water? How will you use the water?”

## Slide 10: Common Filing Mistakes
Proper ownership
  Division’s records
  Share holder
  Contract owner
Need to complete a segregation
Proper evaluation of the water right

## Slide 11: Intro to Public Land Survey

## Slide 12: Township, Range, and Section
  Township—Typically a six-mile square area of land containing 36 sections.
  May also refer to a North-South row in the PLSS grid
  Range—An East-West row in the PLSS grid
  Section—Typically a one-mile square area, containing 640 acres.
Notes: Typical townships and sections
Rivers, lakes, mountains, state borders are a few things that can cause irregular townships and sections

## Slide 13: Typical Corner Sections and Quadrants
NW
W
S
E
N
NE
SE
SW

## Slide 14: Utah Base & Meridians
Salt Lake B&M
  Beginning in Downtown Salt Lake
Uintah B&M
  Beginning about nine miles North of Roosevelt

## Slide 15
Roosevelt,
Duchesne County
  Township 4 South, Range 5 West, USB&M
Stockton,
Tooele County
  Township 4 South, Range 5 West, SLB&M
Notes: What problems this can cause:
Increase time to a decision by a month or more, if advertised incorrectly
Could require a change application to be filed to correct the description (Another filing fee for a change app and more time)

## Slide 16: Marking a Point of Diversion
E
SE
NW
Locate the following:
  S 500’ and W 1200’ from the East Quarter Corner
  N 2000’ from the Southeast Corner
  S 1300’ and E 4000’ from the Northwest Corner

## Slide 17: Marking a Place of Use
Locate the following:
  NW1/4 of the NW1/4
  S1/2 of the SW1/4
  NE1/4 of the SW1/4
  S1/2 of the NW1/4 and the S1/2 of the NE1/4

## Slide 18: Water Right Calculations

## Slide 19: Common Terms
Cubic Feet per Second (CFS)
  A unit of measure used to quantify the rate of flow from a water source
  Area(feet2) * Velocity (feet per second)
Acre-Feet (AF)
  A unit of volume defined as one acre of surface area to a depth of one foot.
  Depth of Water (feet) * Area (acres)
Notes:   CFS=Equal to a volume of water one foot high and one foot wide moving at a velocity of one foot in one second.

## Slide 20: Duty Calculations
Irrigation
  Acres * Duty = AF per Year
  Irrigation duty values vary by area
Domestic
  Full time = 0.45 AF per Year
  Part time = 0.25 AF per Year
Livestock (ELU)
  1 ELU = 0.028 AF per year
  1 ELU = 1 Cow or Horse
  1 ELU = 5 Pigs, Sheep, or Goats
Notes: The maximum volume of water allowed per year for a particular beneficial use.
For irrigation, the duty value varies from area to area within the state.

## Slide 21: Sample Problem #1
A rancher wants to start a farm near Dugway, Utah (area 16). How much water does he need for 5 acres of irrigation, 50 cattle year-round, and a full-time home?
The irrigation duty in Dugway is 4 acre-feet/acre
  5 acres * 4 acre-feet/acre = 20 acre-feet
  50 cattle * 0.028 acre-foot = 1.4 acre-feet
  1 full-time home = 0.45 acre-foot
  Total diversion = 21.85 acre-feet
Notes: These samples are diversion only, to practice converting between units

## Slide 22: Sample Problem #2
A rancher has a water right for 300 cattle. How many sheep could he provide for with this water right?
300 cattle * 5 = 1500 sheep

## Slide 23: Sample Problem #3
A developer wants to build a 10 lot subdivision in Delta, Utah (area 68). Each lot is supposed to have enough water for 0.25 acre of irrigation, 2 horses, and a full-time home. How much diversion will the water right need to have?
  Each lot requires
    0.25 acre * 4 acre-feet/acre = 1.0 acre-foot
    2 horses * 0.028 acre-foot = 0.056 acre-foot
    Full-time home = 0.45 acre-foot
    Total of 1.506 acre-feet
  Total project requires
    1.506 * 10 lots = 15.06 acre-feet

## Slide 24: Sample Problem #4
A farmer has a water right in Brigham City (area 29) that serves 150 cattle year-round. He wants to change the water right to supply one full-time home, one part-time home, 10 horses, and irrigation for his yard. What is the maximum area (in acres) that can be irrigated, after the other uses are accounted for?
    150 cattle * 0.028 acre-foot = 4.2 acre-feet
    Full-time home = 0.45 acre foot
    Part-time home = 0.25 acre foot
    10 horses * 0.028 acre-foot = 0.28 acre foot
    4.2 acre-feet - 0.98 acre-foot = 3.22 acre-feet
    3.22 acre-feet / 4 acre-feet per acre = 0.805 acre
Notes: Sample of Diversion and Depletion
Water right is for 2.0 acres of irrigation (duty 4) = 8.0 AF
Change to livestock
8.0 with a depletion of 50% = 4.0 AF of depletion
Livestock is 100% depletive so the allowable diversion for a change app would be 4.0AF
Historic use of irrigation would have been 8.0 AF of diversion and 4.0 AF of depletion
142.86 ELU (proposed change) would allow 4.0 AF of diversion and 4.0 AF of depletion
Without diversion adjustment the historic depletion would have been exceeded, enlarging the water right.

## Slide 25: Diversion vs Depletion
Diversion is the water removed from the source to be used.
  E.g. Diverting 4.0 AF of water to irrigate 1.0 acre of land
Depletion is the amount of water that is consumed after application.
  E.g. After diverting 4.0 AF of water to irrigate 1.0 acre only 2.0 AF of water returns to the natural water system.
When evaluating Change Applications the State Engineer looks at the historical values for both diversion and depletion.
  Neither value can be enlarged.
Notes: 4.0 AF (Diversion)
Convert to livestock = ~143 cows
2.0 AF (Depletion)
Converts to livestock = ~71 cows
  Water used up by the plants, bound to soil, and lost through evaporation, is water that doesn’t make its way back to the natural water system enabling other water rights to be satisfied.

## Slide 26: Sample Problem #5
A water right owner has a water right for 3.0 acres of irrigation (duty is 4 feet per acre). He wants to change the use to include 50 cattle. How many acre-feet of water will he be able to divert after the change? Assume the rate of depletion for irrigation is 53%.
  Establish historic diversion and depletion
  3.0 acres * duty of 4 = 12.0 acre-feet (diversion)
  12.0 acre-feet * 53% = 6.36 acre-feet (depletion)
  Figure proposed uses
  50 cattle * 0.028 acre-foot = 1.4 acre-feet (100% consumptive)
  6.36 acre-feet – 1.4 acre-feet = 4.96 acre-feet depletion left
  4.96 acre-feet / 53% = 9.36 acre-feet remaining diversion
  9.36 acre-feet / duty of 4 = 2.34 acres of irrigation
  1.4 acre-feet + 9.36 acre-feet = 10.76 acre-feet of diversion
Notes: Using Kamas Station for annual irrigation of alfalfa 19.29 inches or 1.6 feet, based on Dr. Hill’s Crop Consumption research.

## Slide 27: Summary of Diversion and Depletion Limits
Historical Use | Diversion | Rate of Depletion | Amount of Depletion
Irrigation: 3.0 acres | 12.0 acre-feet | 53% | 6.36 acre-feet
Totals | 12.0 acre-feet |  | 6.36 acre-feet
Proposed Use | Diversion | Rate of Depletion | Amount of Depletion
Irrigation: 2.34 acres | 9.36 acre-feet | 53% | 4.96 acre-feet
Livestock: 50 ELU | 1.4 acre-feet | 100% | 1.4 acre-feet
Totals | 10.76 acre-feet |  | 6.36 acre-feet
Notes: Without considering depletion the diversion would have looked like: 10.6 acre-feet for irrigation (2.65 acre)

## Slide 28: Diversion Based Change Applications
Why it feels like a “haircut”
  In this scenario depletion is exceeded by 0.66 acre-foot
Historical Use | Diversion | Rate of Depletion | Amount of Depletion
Irrigation: 3.0 acres | 12.0 acre-feet | 53% | 6.36 acre-feet
Totals | 12.0 acre-feet |  | 6.36 acre-feet
Proposed Use | Diversion | Rate of Depletion | Amount of Depletion
Irrigation: 2.65 acres | 10.6 acre-feet | 53% | 5.62 acre-feet
Livestock: 50 ELU | 1.4 acre-feet | 100% | 1.4 acre-feet
Totals | 12.0 acre-feet |  | 7.02 acre-feet
Notes: Without considering depletion the diversion would have looked like: 10.6 acre-feet for irrigation (2.65 acre)
The State Engineer’s office evaluates diversion and depletion on all change applications. Most applications come in based on diversion only. When the final order is issued the applicant may feel like water was taken away from him because it was not expected nor understood.

## Slide 29: Making an Application Map

## Slide 30: Using the Division’s Website to Get a Point of Diversion (POD)
Be able to locate the property from an aerial map.
Know the approximate location where the well or point of diversion will be located

## Slide 31: Application Map Wizard
Access from the application/form link on the Division’s Website.
Allows a user to select a point of diversion and place of use from an aerial photo and print a map to accompany an application.
Can be generated with signature lines.
Not acceptable as a proof map.

## Slide 32: Sample Application Map

## Slide 33: Researching with Map Search (ESRI)
Ranges on Aerial
Sections on Topo
Notes: Show base map features
Show POD features
Show heretofore and hereafter points

## Slide 34: Layers and Search Tools

## Slide 35: Summary and Wrap-Up

## Slide 36: Topics Covered
Elements common to all applications
Intro to the Public Land Survey System
Basic water right calculations
How to use the Division’s website to create an Application Map

## Slide 37: Questions?